## Slide 1: Adruino Basics
Ардуино осноВИ
gevelichkov@gmail.com

## Slide 2: Съдържание
Запознанство с Ардуино
  Микрокотролери
  История и философия на Ардуино
  Видове Ардуино
  Видове памет
Електричество
  Свързване на светодиод
  Обща теория
Meet your kit
Правила за безопасност

## Slide 3: Запознанство с Ардуино. Основи на електрониката. Микрокотролери
Микрокотролери
  История и философия на Ардуино
  Видове Ардуино
  Видове памет

## Slide 4: микроконтРолери
Малки компютри
Имат GPIO пинове
Широко приложение в техниката
Изпълняват конкретна програма
Работят с различни сензори и акуатори.

## Slide 5: История и философия на Ардуино
Стартира 2003 като проект за студенти
Interaction Design Institute Ivrea
GNU General Public License (GPL),

## Slide 6: Massimo Banzi, David Cuartielles, Tom Igoe, Gianluca Martino, and David Mellis

## Slide 7: ARDUINO UNO
Microcontroller ATmega328P
Operating Voltage 5V
Input Voltage (recommended) 7-12V
Input Voltage (limit) 6-20V
Digital I/O Pins 14 (of which 6 provide PWM output)
PWM Digital I/O Pins 6
Analog Input Pins 6
DC Current per I/O Pin 20 mA
DC Current for 3.3V Pin 50 mA
Flash Memory 32 KB (ATmega328P)
of which 0.5 KB used by bootloader
SRAM 2 KB (ATmega328P)
EEPROM 1 KB (ATmega328P)
Clock Speed 16 MHz
LED_BUILTIN 13
Length 68.6 mm
Width 53.4 mm
Weight 25 g

## Slide 8: ARDUINO MEGA

## Slide 9: Arduino PRO Mini
ATMEGA 328
14 I/O pins
6 analog
Clock 8 mhz
Flash 32 kb

## Slide 10: Arduino Primo wi Fi
WI FI module
Bluetooth
NFC
GPIO expander
Digital I/O 20 pins
3 PWM outputs
Notes: https://www.cnx-software.com/2016/05/19/arduino-primo-board-supports-wifi-bluetooth-le-and-nfc/
https://store.arduino.cc/arduino-primo
45 Euro

## Slide 12: MemORY
Flash memory (program space), is where the Arduino sketch is stored.
SRAM (static random access memory) is where the sketch creates and manipulates variables when it runs.
EEPROM is memory space that programmers can use to store long-term information.
Notes: https://www.arduino.cc/en/Tutorial/Memory
Atmega328
Flash 32k bytes (of which .5k is used for the bootloader)
SRAM 2k bytes
EEPROM 1k byte

## Slide 13: ARDUINO IDE
https://www.arduino.cc/en/Main/Software
Notes: https://www.arduino.cc/en/Reference/Libraries
http://www.fritzing.org/

## Slide 14: SCHEMATIC

## Slide 15: Електричество

## Slide 16: Електричество

## Slide 17: Електричество

## Slide 18: Електричество Закон НА ОМ
U = I * R
Notes: https://learn.sparkfun.com/tutorials/voltage-current-resistance-and-ohms-law

## Slide 19: Свързване на Светодиод

## Slide 20: Свързване на Светодиод

## Slide 21: Свързване на Светодиод

## Slide 22: Общи електрически символи:

## Slide 24: Резистор

## Slide 25: ДИОДи

## Slide 26: LED inDICATORS
Notes: 220 om.

## Slide 27: ТРАНЗИСТОР

## Slide 28: https://www.arduino.cc/en/Tutorial/Blink

## Slide 29: ТРАНЗИСТОР

## Slide 30: Хардуер За Програмисти
https://softuni.bg/trainings/resources/officedocument/7540/presentation-hardware-for-programmers

## Slide 31: Meet YOUR KIT

## Slide 32: BreadBoard

## Slide 33: ПРавила за безопасност

## Slide 34: DEMO BLINK
Download Arduino CC
Test the demo.